## Slide 1: Winery Cleaning Equipment
Joe Lutomske
enotools.com
12/11/09

## Slide 2: Definition of a Winemaker:
www.thfreedictionary.com
Noun1.winemaker : someone who makes wine
Andrew Meggitt, Winemaker, St. James Winery defines as, “A guy (or girl) who spends half his time cleaning”.

## Slide 3: Why Clean?
Improve product quality
Prevent microbial issues
Reduce the likelihood of cross-contamination between batches
Minimize or eliminate shielding residues or coatings which harbor anaerobic microbes/ bacteria.
Increased productivity
Improved employee safety and morale

## Slide 4: Clothing/ Equipment
Chemicals
Waterproof Boots, clothes, and gloves.
Buckets
Scrub Brushes
Lots of running water- Cold and Hot
Pressure Washer
Spray ball or tank/ barrel washer
Wash- Down Hose
Steam Generator ?
Ozone ?

## Slide 5: Pressure Washers & Hot Water
+
=
Aaquatools KEW Poseidon 7
$4500.00
Bullet- Proof and will get things CLEAN
Aaquatools
Noritz 132M
$4199
Greener.
LP gas or Propane
All brands- Hot carts, etc. $3000-$9000
Pro: Convenient.
Cons:
Diesel Fumes or Electric Hungry

## Slide 6: Areas of the Winery to be Cleaned
Tank Room
Barrel Room
Bottling Room
Crushpad
Restrooms
Parking Lot
Tasting Room
Warehouse

## Slide 7: Tank Room
Floors, walls, ceiling, tanks, hoses, hardware, heat exchanger-
Before and after crush, transferring wine
Hot and cold water
Pressure Washer
Hot Water Heater
Hose Pigs
Tank Cleaner

## Slide 8: Cleaning Tanks

## Slide 9: Tank Cleaners : The Price Ranges
Cost : $2500-$4500
Requires $4,500 pressure washer.
VERY effective. Not water saving.
Cost: $1800
Uses your existing pump to recirculate
Effective, if chemical is used. Saves water.
Cost: $150-$300
High Flow Low Pressure. Pump Driven.
Use with chemical. Recirculate Water

## Slide 10: Bottling Room & Equipment
Bottling lines require strict sanitation for preventing the spread of:
TCA- cork, bottle boxes, or corker jaws, bottle dust
Spontaneous fermentation (Sparkling Baco)
“Brett”
Any other issue stemming from good wine rinsed through dirty equipment.
Cleaning methods:
Manual Labor
Steam
Ozone
Chemicals

## Slide 11: Barrel Room
The barrel room should not smell like a cave!
(“Great Fruit. What a nice vineyard. Interesting.”)
Any time moisture, chlorine, and wood/ paper particles meet: hello, TCA
Avoid using pressure treated wood
Clean the room itself
Clean the barrels
SANITIZE the wine thief between uses; Every time!

## Slide 12: Barrel Cleaners 1
How do you clean your barrels?
(Water, ozone, steam, sulphur, chem- tab?)

## Slide 13: Barrel Cleaners 2
Carlsen Spray Ball
With wand, $300.00
Pump- driven
Aaquatools 360
$2800.00
Requires pressure washer

## Slide 14: Bottling Line Cleaning/ Sanitizing -Hot Water, Ozone*, or Steam?
Cost Unknown
Hot water
160 – 200 degrees f
30 – 15 minutes
Wastes water
Ozone
$1,200- $11,000
Fastest
Medium water use
*Only kills what it touches
Steam Generator
$1200- $4500
Dangerous to flesh
Lower water consumption
15 minutes

## Slide 15: Not All Barrels are Wood

## Slide 16: Ozone
Test the machine on YOUR water
Warranty?
Service?
Training?
REFERENCES

## Slide 17: Q&A